## Slide 1
Systems Engineering Seminar
3/21/19
Matt Garrison, ISE

## Slide 2: Lucy Overview
Trojans are remnants of giant planet formation
  They should be low density and volatile rich below a
  desiccated surface layer with complex surface chemistry.
But they are not a homogeneous population
  Contain C-, D-, and P-type spectral types
  Have visible albedos from ~4 - ~15%
(DeMeo et al.)
(Grav et al.)
Trojans are very diverse, which makes them particularly exciting
  None have been viewed up close
  Wide range of colors.
(Emery et al.)
2

## Slide 3: An Amazing Trajectory
We have found a trajectory that visits 6 Trojans and 1 Main Belt Asteroid.
Lucy’s unique trajectory is the key aspect of the mission
Notes: Walk through the Lucy trajectory in a Frame rotating with Jupiter with sun/jupiter line fixed

## Slide 4: An Amazing Trajectory
We have found a trajectory that visits 6 Trojans and 1 Main Belt Asteroid.
Lucy’s unique trajectory is the key aspect of the mission
Notes: Walk through the Lucy trajectory in a Frame rotating with Jupiter with sun/jupiter line fixed

## Slide 5: An Amazing Trajectory
We have found a trajectory that visits 6 Trojans and 1 Main Belt Asteroid.
Lucy’s unique trajectory is the key aspect of the mission
Notes: Walk through the Lucy trajectory in a Frame rotating with Jupiter with sun/jupiter line fixed

## Slide 6: An Amazing Trajectory
We have found a trajectory that visits 6 Trojans and 1 Main Belt Asteroid.
Lucy’s unique trajectory is the key aspect of the mission
Notes: Walk through the Lucy trajectory in a Frame rotating with Jupiter with sun/jupiter line fixed

## Slide 7: Lucy Overview
Planetary mission: Schedule is king!

## Slide 8: Payload and Spacecraft
L’LORRI
LOng Range Reconnaissance Imager (LORRI)
High spatial resolution visible imager
Heritage: NH
TTCam
Terminal Tracking Camera (TTCam)
Visible imager used for target centroiding
Supplier: Malin Space Systems
L’TES
Thermal Emission Spectrometer (TES)
Point FTIR spectrometer Heritage: O’REX, MGS
Multi-spectral Visible Imaging Camera (MVIC)
Linear Etalon Imaging Spectral Array (LEISA)
Color visible imager (MVIC) and infrared imaging spectrometer (LEISA)
Heritage: NH, O’REX
L’Ralph
SC Telecommunications link with DSN provides Doppler measurements which enable mass density determination of each trojan
SDST Heritage: MAVEN/OREx/InSight
Radio Science
Notes: 3 instruments accommodated on IPP, instruments coaligned for target viewing
IPP has 2 ranges of motion on a gimbal (pitch yaw, horiz, vert direction) 2 dOF to handle PM binary and keep the instruments pointed at the target based on ephemeris updates and performs surface motion compensation.
SC in deployed position, RF system is used for science – mass densities of the Trojans can be determined on the ground using DSN Doppler data as part of the radioscience.
TTCam used for terminal tracking near closest approach to do autonomous fine pointing as Lucy acquires the trojan targets, need TTCam to take out residual navigation delivery error

## Slide 9: Encounters
X
Z
Y
Trojan
Sun
Shows relative
motion during a
”feet-first” encounter.
Spacecraft tracks the target Trojan and IPP handles precision pointing
  SC target tracks in a nadir pointed attitude
  IPP surface tracks and precision points

## Slide 10: L’Ralph Overview (Summary)
Surface FOV
Dichroic
LEISA Detector
MVIC
Detector
Color Filter
LVF
Main
Electronics
Box
(MEB)
FPE-VIS
FPE-IR
LEISA
Detector
Data
MVIC
Detector
Data
Detector
Fold
M2
M3
M1
Scan
Mirror
Mechanism
(SMM)
Scan
Fold
MVIC
Detector
Data
TDA
Instrument Description | L’Ralph combines a VIS/NIR multispectral and panchromatic imager (MVIC) with a SWIR spectral mapper (LEISA).
Instrument Mass | 29.4 kg CBE (21% margin)
Instrument Power | 24.3 W CBE (19% margin)
Field of View | 145 mrad x 56 mrad
Scan Angle | 140 mrad
MVIC IFOV | 29 mrad
LEISA IFOV | 80 mrad
LEISA Wavelength | 0.95-3.95 μm
MVIC Wavelength Bands | Band 1: Panchromatic (370-905) Band 2: 375-480 nm Band 3: 480-520 nm Band 4: 520-625 nm Band 5: 625-750 nm Band 6: 750-900 nm
Calibration | Solar Cal, Filament and Black Body

## Slide 11: L’Ralph Physical Design

## Slide 12: L’Ralph Driving Requirements
ID | Requirement | Drives
LR-INST-12 | The L'Ralph instrument shall scan the FOV along-track with a range >=140 mRad. These angles are the optical angle; mirror angles are 1/2x the values given. | Scan mirror, scan mirror sensors
LR-INST-09 | The L'Ralph instrument shall provide a LEISA ensquared energy specified in Table 1 over the wavelength range from 1.0 to 3.4 um. | Optical design, alignment, stability, scan accuracy
LR-INST-10 | The L'Ralph instrument shall provide a MVIC ensquared energy specified in Table 2 over the wavelength range from 0.40 to 0.90 um. | Optical design, alignment, stability, scan accuracy
LR-INST-20 | The L'Ralph LEISA shall have an SNR > 25 for spectral features with FWHM of 0.07 um in the range 1.0-3.4 um given an input source of the black body spectrum and the allowed time for scans. | Optical through-put, QE, electrical noise, TDA temperature
LR-INST-28 | The L'Ralph MVIC shall have an SNR > 25 in each color channel given an input source of the black body spectrum and the allowed time for scans. | Optical through-put, QE, electrical noise
Dark Target
See Features

## Slide 13: Block Diagram

## Slide 14: Requirement Status

## Slide 15: L’Ralph Field of View
Not to scale. Locations are approximate.
LVF1
0.952-1.615um
LVF2
1.541-2.605um
LVF3
2.57-3.95um
Band 6
Band 5
Band 4
Band 3
Band 2
Band 1
LEISA
MVIC
Scan Direction
Cross-Track
Along-Track
Shown to scale.
Band Definitions
Band 6: Panchromatic
Band 1: 0.375-0.480um
Band 2: 0.480-0.520um
Band 3: 0.520-0.625um
Band 4: 0.625-0.750um
Band 5: 0.750-0.900um

## Slide 16: State Diagram
OFF
Htrs On/Off
DECON
BOOT
STANDBY
MVIC Cal
MVIC Sci
LEISA Sci
LEISA Cal
Power On
Boot complete
Command
Any state can go to OFF through unannounced removal of power
Completed

## Slide 17: MVIC Data Flow
FPE-Vis
Buffer
FPGA Command Processing
Spacecraft
Read Request
Raw Image Data
M4
Read Request
MCE
Buffer
Position Data
Images
C&DH
Positions
EDAC
EDAC
Pan and color

## Slide 18: LEISA Data Flow
FPE-IR
Buffer
FPGA Subtraction
FPGA Command Processing
Spacecraft
Read Request
Raw Image Data
EDAC
M4
EDAC
Read Request
MCE
Buffer
Position Data
Images
C&DH
Positions
FPGA Super-Pixeling
CDS Image Data

## Slide 19: LEISA Processing
FPE reads 512x1472p reset frame (start of integration)
FPE reads 512x1472p image frame
(end of integration)
H2RG channels arranged horizontally
<= 23 of the 32 channels read out by FPE
H2RG Columns
H2RG Rows
Mode
Processed or CDS
Raw
M4 stores image and reset frames
C&DH subtracts reset from image to get 512x1472p CDS frame
(Correlated Double Sampling)
C&DH bins pixels into 2x2 super-pixels to get 256x736p reduced frame
C&DH transmits CDS frame
C&DH eliminates dead pixels per map
Mode
CDS
Processed
C&DH transmits Processed frame
Bad Pixel Map?
Yes
No
M4 stores CDS frame
Read Request from Spacecraft

## Slide 20: Lucy Org Chart
SCIENCE
Project Scientist (Noll/GSFC)
Deputy PS (Marchi/SwRI)
Communication and Public Engagement (Kretke/SwRI)
Office of Communications
(Neal-Jones/GSFC)
Principal investigator
PI (Levison/SwRI)
Deputy PI (Olkin/SwRI)
Management Advisory Group
(Burch/SwRI), (Scolese/GSFC), (Callahan/LM)
Safety & Mission Assurance (GSFC)
CSO (Haskell)
EEE Parts (Williams)
Reliability (Knapp, Alimardani, Sindjui)
Materials (Mohammed)
Radiation (Casey)
Safety (Hill)
S/W QE (Whitelock)
H/W QE (Dimarco, Knight, Ott)
Procurement
Aqueche, Moore/GSFC
Project Management
PM (Donnelly/GSFC)
DPM (Douglas-Bradshaw/GSFC)
DPM/R (Elliott/GSFC)
Payload DPM (Andrews/SwRI)
Launch Segment
LSM
(Carson/GSFC)
LSP/MIM
(Calero/KSC)
L’LORRI (APL)
IPI (Weaver)
DPI (Dello Russo)
IPM (Adams)
IS (Spencer/SwRI)
ISE (Wilson)
L’TES (ASU)
IPI (Christensen)
DPI / IS (Hamilton/SwRI)
IPM (Patel)
ISE (Mehall)
L’Ralph (GSFC)
IPI (Reuter)
DPI (Simon)
IPM (J. Simpson)
DIPM (Dolch)
IS (Howett/SwRI)
IS (Grundy/Lowell)
ISE (Garrison)
Project Office (GSFC)
Finance (Bradel, Crigger, Bond)
Project Support (Pszcolka, McCall)
Scheduling (Rogers, Hegarty)
EVM (Smith)
CM/DM (R. Berry, Prats)
Systems Engineering (GSFC)
PSE (Thompson)
Deputy PSE (Sekerak)
SC Systems Lead (Hageman)
Payload SE (Vincent/SwRI)
Contamination Ctrl (Lorentson)
Encounter SE (Starin)
Risk Manager (Tillard)
Con Ops (Wasiak)
Verification & Validation (Pevear)
S/W Systems Manager (Wilson)
Launch Vehicle (Carson)
Spacecraft
SC Manager (Jenkens/GSFC)
PM (Halbrook/LM)
Eng Mgr (Lipe/LM)
CSE (Altonen/LM)
Ground & Operations
GS&O Manager (Wasiak/GSFC)
SOC (Parker/SwRI)
MOC (Effertz/LM)
NOC (Hoffman/KinetX)
DSN (Monson/JPL)
Payloads
FLIGHT DYNAMICS
FD Lead (K. Berry/GSFC)
Navigation (Stanbridge/KinetX)
Mission Design (Sutter/LM)
Optimization (Englander/GSFC)

## Slide 21
Instrument | Payload | Mission or Spacecraft
Risks
Risks
Oversight
L2 Requirements
L3 Requirements
Oversight
ICD
ICD
Oversight
GOLD Compliance
GOLD Compliance
Inputs
Payload Con Ops
Mission Con Ops
Inputs
Resource Request
Resource Requests
Payload Office and PLSE Role
Resource Allocations
Resource Allocations
Payload CCB
Inst. Applicability
GOLD Rules
Requirements
ICDs

## Slide 22: L’Ralph Org Chart
L’Ralph’s Org Chart shows clear lines of responsibility

## Slide 23: Flexible Fault Management
Since we can never revisit a target…
…We want to make sure we don’t go into safehold during a critical time
  Instrument is tasked with identifying faults but not safing itself, just sending a “safe me” message to the spacecraft
  Depending on project risk posture and encounter timeline, the spacecraft may be configured to reset the instrument, switch sides, or do nothing
  Side-effect: we’ve had to add this fault management into our GSE since the instrument can’t safe itself

## Slide 24: Memory Redundancy
Since we can never revisit a target…
…We want to make sure that science data isn’t lost or corrupted
  Instrument records science data on flash memory in the MEB
  Instrument sends a copy of that science data to the Spacecraft as soon as possible, but maintains the original copy until the group commands it to erase
  If an error in science data is found on the ground, science data can be replayed from spacecraft memory OR instrument memory
  Cross-strapping allows the spacecraft to access science data from either side of the instrument

## Slide 25: Saving More Than We Need
Since we can never revisit a target…
…We can’t decide we want more data than we took
  Instrument records LEISA data in CDS format before super-pixeling
  Super-pixeled data is sent to the spacecraft and ground
  Un-summed data is maintained in instrument memory in case the ground later requests higher-resolution data
  Instrument records all 6 MVIC bands for all observations
  Only the desired bands are sent to the spacecraft and ground
  All bands are maintained in instrument memory in case the ground later requests the others

## Slide 26: Mass Threat Burn-Down
Since we launch on an interplanetary trajectory…
…Mass has to be tightly managed
Mass threats/opportunities were tracked from SRR through December 2018 (when the final mass threat was retired)
  Initial estimates ranged from -2kg to +6kg, with a probability-weighted average of 2.8kg MEV
  Final realized mass change was 2.9kg MEV

## Slide 27: Ralph Technical Reporting
Mission Systems
Mission
PI
Payload Systems
Ralph Systems
Core MEB
SE
Spacecraft Systems
Mission
PI
Payload Systems
Core MEB
SE
Mission Systems
Ralph Systems
Same hallway
Same hallway
Same group lead
1700 miles Away
PIMS
PIMS
TDMS
TDMS
Sharepoint
DOORS
FSW
Lead
Confluence
Former same group lead
1620 miles Away

## Slide 28: Different Info in Different Homes
TDMS
L3, L4 requirements
Typically-CM’ed stuff (plans, procs, reports, analyses, etc)
Risks
PIMS
SwRI RFAs
SwRI CM
Payload change requests
Flight rules
Sharepoint
Rec/Del List
Pointing information
Spacecraft tech info
Confluence
FSW requirements
FSW design details
DOORS
L3 requirements
L3 verification
Ralph Systems
Core MEB
SE
Auto
Password
Password
Badge + PIN + 2xPassword
Badge + PIN + Password
Auto
Password
2x RSA Token + 2x Password
SwRI can’t access their own systems while VPN’ed into GSFC for TDMS

## Slide 29: Project Change Process
Project Systems
Payload
Spacecraft
Change Originates
Informal Change Paper Generated, Vetted with Systems Engineering working group
Word
PowerPoint
DOORS Output
PSE/CSE Vets Change Paperwork
CRB Reviews Change Request
DOORS Administrator inputs Proposed Change(s) in DOORS
From/To CCR generated via DOORS export, input to TDMS as Pre-LM SDT CCR
DOORS Administrator
CCR to drive new Revision in TDMS
Supports contract dates
Incorporates all approved From/To CCRs
Full document generated via DOORS export
CRB may:
Approve
Reject
Approve with adjustments
Proceed via PSE direction
Released when Approved
CCR Approved in TDMS
CCB Approval
Responsible SC SE receives direction from CCR
CCRs Collect and await next release per Contractually driven dates
Update Requirements in DOORS based on CCR
SDT to review CR (derived from the Lucy CCR) impacts and adjust other documentation or other impacts accordingly
ECB to review LM CR for approval

## Slide 30: Controlling Communication
Conscious effort to maintain lines of communication
  If the MSE and I work something out in the hallway, we typically call/email the payload systems engineer for his take on things
Lots of standing meetings:
  PDL one-on-ones, Payload to L’Ralph tagup, Payload weekly, SC ICD working group, SEWG, SDT…
Technical reviews are faster if you email the files to non-GSFC teammates and they email their approval or comments back to the originator and CM
  Faster response time but risk of multiple unofficial versions living in email
Continuing effort to improve our processes

## Slide 31: Meetings and Communication
Communication is regular and efficient
Meeting | Owner | Participants | Topics | Cadence
L’Ralph team meeting | IM | PDLs, SE team, PIs, IM | Status, concerns, announcements | 1/week
L’Ralph Technical Topics | ISE | PDLs, SE team, PIs | Announced special topics | 2/week
Risk Board Meeting | IM | SE team, PIs, IMs | Risks, issues | 2/month
MEL Control Board | ISE | PDLs, SE team, PIs, IM | Mass and Power MEV increases | 1/month
PDL 1-on-1s | IM | PDL, ISEs, IMs | Status, concerns | 2/month/PDL
Payload/L’Ralph Weekly | Payload Manager | Payload, ISEs, IMs, PIs | Status, concerns, CRs | 1/week
Payload Weekly | Payload SE | Payload, ISEs, IMs, PIs, other instruments | Cross-payload topics | 1/week
Spacecraft ICD Working Group | ISE | Payload SE, ISEs, SC SE | Spacecraft ICD special topics | 2/month

## Slide 32: Tech Topics
No standing systems team meeting outside of weekly L’Ralph team meeting
Tech topic meeting structure
  2x a week
  Whole team is invited
  At least a day ahead of time, a topic is announced and the invitation list is pared down to only the required people
Example topics are:
  Future plans (ETU MEB to EM detector interface test planning)
  Work problems (FPE power growth and possible design solutions)
  Close trades (SC thermal harness design decision)

## Slide 33: Concerns Process
Concerns process is used to capture any concerns that could impact operations, performance, requirements verification, or the availability of hardware.
Captures items that can’t be solved in a single discussion; some concerns have a long horizon based on the planned availability or need date of information.
Example concerns:
  Questions tabled until later (Need to determine if GSE mounting plate for TVac needs active cooling)
  Problems being worked (MVIC video signal characteristics and optimized gains)
  Pre-risks (Imported jitter from spacecraft might be too high for mechanism)
Concerns, status, and closure are logged on a SharePoint Action Item site that is accessible by anyone within the GSFC firewall
New, near-term, or actively-worked concerns are statused at the L’Ralph team weekly and the weekly report
Closed concerns remain accessible as a record of outcome

## Slide 34: Polling for Process Improvement
After each major review, we’ve polled the whole team:
  What went well?
  What didn’t?
  What could we do to improve?
Answers were anonymously gathered and sent to ISE
Discussed with PI, dPI, IPM, dIPM
There is a professional group on center that will help do this for larger teams

## Slide 35: After SRR
Weekly technical special topic meetings work well paired with statuses from the weekly team meeting
A detailed scrub of the MEL right before SRR found significant missing mass. This should have been done sooner.
Communications with the spacecraft team through the payload office led to errors and miscommunications. Set up a bi-weekly spacecraft ICD discussion with spacecraft systems and payload systems.

## Slide 36: After PDR
Systems participation in bi-weekly PDL one-on-one meetings were a good venue to understand progress and concerns
Systems concerns process helps organize cross-disciplinary and long-term problems
TDMS access for off-site PDLs has been difficult. For near-term reviews, have to email them the file and have them email response to CM
Some weekly status meetings are run without agendas or announced topics, aren’t very efficient
Discipline SEs (thermal, mechanical, electrical, optical, contam) need to be comfortable reaching out to the PDLs; PDLs need to seek them out for discipline-specific guidance
PDLs spend a lot of their day on programmatic planning and statusing; IPM and dIPM streamlined process with PDL one-on-one meetings

## Slide 37: Conclusion
Lucy is a cool mission to the Trojans enabled by a twice-in-a-lifetime trajectory
L’Ralph is a critical, multi-purpose science instrument
The mission architecture has driven specific features into the instrument design
The project organization has forced us to be more strategic in planning communications
L’Ralph is starting to build flight hardware