## Slide 1: Evolved Structures: Generative Design and Digital Manufacturing at GSFC
Ryan McClelland
Research Engineer
Instrument Systems and Technology Division
(ISTD, 550)
NASA Goddard Space Flight Center (GSFC)

## Slide 2: Context
Developed on NASA Goddard Internal Research funding (IRAD)
  Goal: create and infuse a broadly applicable process to rapidly develop lightweight spaceflight structures
  Method: build and test parts for diverse NASA applications
  Status: development of typical metallic structures now automated
    Requirements➡parts for fab in 1-2 days(!)
    Demonstrated by test
    Being applied to NASA missions and proposals: CCRS, DraMS, DAVINCI, EXCITE, LEXA, HWO, STRIVE, etc
Goals of this presentation
  Enable missions to improve the mass/stiffness/strength of structures by 2x-4x while reducing development time/cost by ~10x
  Inform stakeholders on how to identify promising applications
  Help GSFC win missions and deliver on commitments
  Share lessons learned for successful mission infusion
"Not every change is an improvement, but every improvement is a change"

## Slide 3: Inspiration
Image source: https://expanse.fandom.com/wiki/Tycho_Station?file=Tycho-stn-3.png
“AI is one of the most important things humanity is working on. It is more profound than, I dunno, electricity or fire,”
-Sundar Pichai (Google CEO)
Image source: https://en.wikipedia.org/wiki/Millennium_Falcon
Image source: https://www.artstation.com/artwork/Z5lYJm
Image source: https://mobile.twitter.com/aebdigital/status/1079504882393116674

## Slide 4: Evolved Structures Process
(1) Digitally encode structure requirements into software
  Follow written Evolved Structures Guide for NASA applications
(2) Use Generative Design AI to evolve optimal designs meeting requirements
  Using COTS software adapted for GSFC needs
(3) Fabricate parts directly from Generative Design output using Digital Manufacturing (software + robots)
  Using industrial processes such as automated CNC and Additive Manufacturing (AM)
Encode Requirements
~1 hr
Evolve Designs
~1 hr
Fabricate Parts
1 day – 3 weeks
Input: Requirements ▶ Output: Parts

## Slide 5: Benefits of Evolved Structures Process
Help GSFC win missions
  2x-4x improved performance (mass/stiffness/strength)
  10x reduced development time/cost
  Virtuous cycle 🔄 lighter designs need lighter support structure
  Lower mass = lower cost
  Currently a unique capability of Goddard
Help GSFC deliver on funded missions
  Solve mass challenges
  Work more efficiently ▶ get more work done
Use modern computing to reduce tedious work so engineers can focus on challenges
Achieve more science per dollar
We can not build the ambitious missions of the future with the tools of the past

## Slide 6: NASA EXoplanet Climate Infrared Telescope (EXCITE, PI: Peter Nagler)
Image Source: https://www.jpl.nasa.gov/news/nasa-mission-will-study-the-cosmos-with-a-stratospheric-balloon
40 km above Earth’s surface
Telescope
Tip/Tilt assembly
Notes: Source Link: need to add paper from EXCITE
https://arxiv.org/abs/1903.09718
Will update weight + balloon – 1.5t to be updated, 400 ft to be updated,
Long Duration Balloon (LDB)
Check mass figure – may be 50-75%

## Slide 7: Application Example: EXCITE Tip/Tilt Bracket
Mission: Analyze atmospheres of exoplanets
Goal: Mount Tip/Tilt mirror assembly to the back of the Telescope (PI: Peter Nagler)
Interfaces: Bolt pattern on Tip/Tilt stage and bolt pattern on Telescope. Avoid Tip/Tilt assembly volume and optical path.
Loads: 10g vertical (x) 3g lateral(y and z) applied to Tip/tilt stage center of gravity (1.35 kg mass)
Modes: >100 Hz per standard practices and to avoid cryo-cooler excitation
Bracket mass target: 0.2 kg
Telescope
Tip/Tilt assembly

## Slide 8: Application Example: Human Design
Design problem given to senior design engineer
Finite Element Analysis (FEA) done my me
  Design improved with iteration
No manufacturable design meets the mass target
Elapsed time: 2 days
Human Designer Iteration | 1 | 2 | 3 | 4
Design (Aluminum) |  |  |  | 
Mass (kg) | 0.59 | 0.18 | 0.27 | 0.18
1st Mode (Hz) | 137 | 37 | 65 | 108
Stiffness/mass (Hz/kg) | 232 | 205 | 240 | 600
Max Stress (MPa) | 26.3 | 189 | 103 | 60.7
Manufacturing | CNC | CNC Difficult to machine hog-outs – no quote | CNC Difficult to machine hog-outs – no quote | Not machinable/ printable– no quote

## Slide 9: Application Example: Evolved Structures Design
Designer | Expert Humans (2X) | AI CNC | AI AM
Design |  |  | 
Design time | 2 days | 1 hour | 1 hour
Design iterations | 4 | 31 | 31
Mass (kg) | 0.27 | 0.2 | 0.2
1st Mode (Hz) | 65 | 147 | 177
Max Stress (MPa) | 103 | 14.8 | 11.2
Manufacturing | CNC - Difficult to machine (no quotes) | Automated CNC $1000 3 days | L-PBF AM $2000 3 weeks
Obstacles (red)
Preserves (green)
Load
Constraints
Outputs
Inputs
VALIDATED
Notes: Validate with existing methods. Same as you do with human designs!

## Slide 10: Case Study: EXCITE Evolved Optical Bench

## Slide 11: Case Study: EXCITE Evolved Optical Bench

## Slide 12: Application Examples
EXCITE: Tip/Tilt mount
EXCITE: Radiator mount
EXCITE: Detector mount
MSR-CCRS: Capture Lid
MSR-CCRS: Capture Sensor Bracket
Venus lander
Optical Bench
CCRS: LTM Paddle
DraMS Carousel Base
“The trick to having good ideas is not to sit around in glorious isolation and try to think big thoughts. The trick is to get more parts on the table.”
- Steven Johnson
Optical Bench
EXCITE: Optical Bench
LEXA: Lunar Spectrometer
Notes: Lesson: first find low hanging fruit, demonstrate value, then scale up

## Slide 13: Case Study: ALICE Evolved Optical Bench
Earth Science Instrument for STRIVE mission
Radically lightweight structure
  Reduced from 3.6 kg to 610 gms!
Consolidates 10 parts from the original design
  CNC machined from a single block of Aluminum
Successfully vibration tested to GEVS standards
Demonstrates Evolved Structures as an enabling technology for future instruments
  Reducing mass creates a virtuous cycle, enabling other parts of the system to be lighter and reducing power consumption, all of which ultimately reduce cost
Next step: reduce entire instrument mass to fit on a smaller mission class
Notes: Example of EXCITE Tip/Tilt Bracket shows game changing improvements in development time/cost (16 hours vs 1), mass/stiffness (3x improvement), stress (4x reduction), and manufacturability. Human design could be improved with further iterations, but it would take weeks.

## Slide 14: Generative Design: Paradigm Shift
Design requirements and goals
Designer creates CAD model
Analyst checks against requirements
Designer generates drawing
Machinist evaluates drawing
Fabrication
Inspection
Qualification
Flight
Design requirements and goals
AI Generates Designs; checks requirements and fabrication
Digital Manufacturing
Inspection
Qualification
Flight
Current GSFC Process
Months-Years
Evolved Structures Process
Hours-Days
Engineer focuses on requirements
Demonstrated: Requirements known to parts in-hand in <2 weeks. 2x-4x lighter.

## Slide 15: Generative Design: How the process works
User inputs
Create voxel mesh of design space
Run Topology Optimization
Output results for user review
Reconstruct CAD model of selected outputs
AI: Computer systems able to perform tasks that normally require human intelligence

## Slide 16: Digital Manufacturing: Robots turning bits to atoms
Atoms
Bits

## Slide 17: Digital Manufacturing
CAD ▶ CAM ▶ Code ▶ Robot ▶ Part
Most of the time CNC is best
  Generative Design creates parts that are fundamentally stiff and machinable
  Commercial CNC capabilities far exceed most engineer’s expectations
  Material properties superior to AM
    More ductile, more predictable
  Vendor suggestions: CNC 5-axis Machine Shop Master List.xlsx
AM (3D Printing) advantages and costs
  More design freedom ▶ greater performance (~10%-20%)
  Fabrication cost lower for expensive-to-machine materials
    Titanium, Inconel, etc
  Material properties are process dependent
  But: Additional verification and documentation required
    NASA-STD-6030 – depends on mission class

## Slide 18: CNC vs. AM for Evolved Structures (Today)
AM generally has cost and schedule disadvantages for aerospace
  Limited choice of AM vendors, especially for parts >250mm
  Material properties process dependent, varies by vendor
  Tolerances are poor compared to CNC – post machining
  Surface finish is rougher than CNC machining.
  Removal of supports requires manual finishing, leading to variable surface quality
  Heat treatment usually required
  Additional testing and inspection required NASA-STD-6030
  Build failures expected
Need a compelling reason to use AM
  Unmachinable features like internal voids and channels

## Slide 19: AM for Evolved Structures (Future)
Cost and schedule will improve due to mature technologies, marketplace, and standards
Generative Design and AM will enable large monolithic structures
  Vastly improved performance
  Vast reduction in part count
JPL
Image source: https://www.wired.com/story/massive-ai-powered-robots-are-3d-printing-entire-rockets/

## Slide 20: Project Infusion: Lessons Learned
Earlier is easier ▶ more design freedom ▶ more mass savings
  Pre-Phase A (e.g. proposal phase) is ideal
    Load path understanding ▶ better structure layout
  Pre PDR-EPR is good, ideally have a physical prototype at PDR-EPR
Virtuous cycle 🔄 compounds the advantages ▶ help win missions
  Lighter designs need lighter support structure and smaller ACS components
  Stiffer designs have less jitter
  Lighter designs have less surface area and/or volume ▶ less heating/cooling ▶ smaller radiators/heaters ▶ less mass/cost
  More science per dollar
Key to success: identify a promising application
  Small to mid-size parts, generally < 1 meter max dimension
  Metallic (Aluminum, Titanium, or Invar)
  Need to support components, detectors, optics, reaction wheels, etc
  Not just replacing a honeycomb plate or composite tube
  Truss layout for larger structures

## Slide 21: Project Infusion: Prototype to Baseline

## Slide 22: Heritage
Topology Optimization techniques developed in the 80s with commercial software integration in the 90s
  Altair OpiStruct
Thales has flown many Generatively Designed parts
  Hundreds flown on commercial missions
  Large antenna brackets flown on NASA SWOT
JPL cable bracket for Europa Clipper
  Qualified for flight (2024 launch)
SpaceX uses Generative Design commonly

## Slide 23: Project Infusion: System-level Analysis
Structural Analyst thinks system-level analysis will be too hard/slow
  Challenges overcome and documented on CCRS LTM Paddle, CLM Arm, and Capture Sensor Bracket
  Fusion 360 can output a NASTRAN FEM directly ▶ work with analyst on meshing
  Four techniques for model reduction
    Reduced tet mesh (e.g. CCRS LTM Paddle, CLM Arm)
    Reduced plate and beam model: Fusion 360 can help
    SuperElement model
    Smeared mass for CLA (Capture Sensor Bracket)
Thermal Analyst thinks system-level analysis will be too hard/slow
  Challenges overcome and documented on CCRS LTM Paddle, CLM Arm, and Capture Sensor Bracket
    Reduced primitive models
  Fusion 360 can create primitive geometry ▶export curves and surfaces
  Fusion 360 thermal analysis can be used to quickly check conductance
Get analyst input as after first design iteration if possible

## Slide 24: Getting Started with a New Application
Evolved Structures Team funded for mission infusion
  Can provide preliminary design and analysis support at no cost
  IRAD funding also available for prototype fabrication
  Sustaining engineering provide by trained project engineers with expert consultation
What to expect:
Application assessment
1 hour
Generative Design Application Checklist
1 hour
Design and analysis provided to project
1-3 days
Feedback or
Req. change
Providing proven technology to expedite development, arriving at a technically superior solutions, for no initial project cost

## Slide 25: Conclusion and Call to Action
Evolved Structures provide significant benefits to NASA missions
  2x-4x improved performance (mass/stiffness/strength)
  10x reduced development time
  Virtuous cycle reduces mission costs: more science per dollar
Ready for broad mission infusion
  Embraced by major GSFC projects
  Infusion process defined by code 500
  Flown on NASA missions
  Complex parts fabricated and tested
Contact the Evolved Structures team to get started

## Slide 26: Training Resources
Evolved Structures Team: Funded for infusion
  ryan.s.mcclelland@nasa.gov, matthew.vaerewyck@nasa.gov
  Generative Design MS Team
  Fusion 360 help channel
Evolved Structures Guide for GSFC Applications: living document
Download and install Fusion 360 trial
  Elevated Privileged not required
  Assess and cleared: CITR SHELF - Commercial IT Request (CITR) (nasa.gov)
Get a full license from the Generative Design Team
Take self-paced free training: Fusion 360 Help | Course: Introduction to generative design | Overview | Autodesk
  Google and Youtube are also good for finding solutions
  More training linked in Evolved Structures Guide